详表

00 AMIDEBUG RX/APTIOAMIDEBUG RX/APTIO

01 PWR ON, RST DETECT 加电，RST检测

02 AP INIT B/F MICRO AP初始化

03 NB INIT B/F MICRO 北桥初始化

04 SB INIT B/F MICRO 南桥初始化

05 OEM INIT B/F MICRO OEM初始化

06 MICROCODE LOADING 微代码加载

07 AP INIT A/F MICRO AP初始化

08 NB INIT A/F MICRO 北桥初始化

09 SB INIT A/F MICRO 南桥初始化

0A OEM INIT A/F MICRO OEM初始化

0B CACHE INIT Cache初始化

0C AMI RESERVED AMI保留

0D AMI RESERVED AMI保留

0E MICROCODE NOT FOUND 微代码没有找到

0F MICROCODE NOT LOADED 微代码没有加载

10 PEI CORE STARTED PEI核心启动（Pro-EFI初始化）

11 PRE-MEM CPU INITPRE-MEM CPU初始化

12 CPU PRE-MEM INIT CPUPRE-MEM初始化

13 CPU PRE-MEM INIT CPUPRE-MEM初始化

14 CPU PRE-MEM INIT CPUPRE-MEM初始化

15 PRE-MEM NB INITPRE-MEM NB初始化

16 PRE-MEM NB INITPRE-MEM NB初始化

17 PRE-MEM NB INITPRE-MEM NB初始化

18 PRE-MEM NB INITPRE-MEM NB初始化

19 PRE-MEM SB INITPRE-MEM SB初始化

1A PRE-MEM SB INITPRE-MEM SB初始化

1B PRE-MEM SB INITPRE-MEM SB初始化

1C PRE-MEM SB INITPRE-MEM SB初始化

1D OEM PRE-MEM INIT OEMPRE-MEM初始化

1E OEM PRE-MEM INIT OEMPRE-MEM初始化

1F OEM PRE-MEM INIT OEMPRE-MEM初始化

2A OEM PRE-MEM INIT OEMPRE-MEM初始化

2B MEM INIT. SPD READ MEM初始化读SPD

2C MEM INIT. MEM DETECTMEM初始化检测MEM

2D PROG MEM TIMING INFOMEM时序信息编程

2E CONFIGURING MEMORY 配置内存

2F MEM INITIALIZATION MEM设定初值

30 ASL RESERVED ASL保留

31 MEMORY INSTALLED 内存安装完成

32 CPU POST-MEM INIT CPUPOST-MEM初始化

33 CACHE INITIALIZATIONCache设定初值

34 APP PROCESSOR INIT APP处理器初始化

35 BSP SELECTION BSP选择

36 SMM INITIALIZATION SMM设定初值

37 POST-MEM NB INITPOST-MEM NB初始化

38 POST-MEM NB INITPOST-MEM NB初始化

39 POST-MEM NB INIT POST-MEMNB初始化

3A POST-MEM NB INITPOST-MEM NB初始化

3B POST-MEM SB INITPOST-MEM SB初始化

3C POST-MEM SB INITPOST-MEM SB初始化

3D POST-MEM SB INITPOST-MEM SB初始化

3E POST-MEM SB INITPOST-MEM SB初始化

3F OEM POST-MEM INIT OEMPOST-MEM初始化

40 OEM POST-MEM INIT OEM POST-MEM初始化

41 OEM POST-MEM INIT OEMPOST-MEM初始化

42 OEM POST-MEM INIT OEMPOST-MEM初始化

43 OEM POST-MEM INIT OEMPOST-MEM初始化

44 OEM POST-MEM INIT OEMPOST-MEM初始化

45 OEM POST-MEM INIT OEMPOST-MEM初始化

46 OEM POST-MEM INIT OEMPOST-MEM初始化

47 OEM POST-MEM INIT OEMPOST-MEM初始化

48 OEM POST-MEM INIT OEMPOST-MEM初始化

49 OEM POST-MEM INIT OEMPOST-MEM初始化

4A OEM POST-MEM INIT OEMPOST-MEM初始化

4B OEM POST-MEM INIT OEMPOST-MEM初始化

4C OEM POST-MEM INIT OEMPOST-MEM初始化

4D OEM POST-MEM INIT OEMPOST-MEM初始化

4E OEM POST-MEM INIT OEMPOST-MEM初始化

4F DXE IPL IS STARTED DXEIPL开始

50 INV MEM TYPE/SPEED INVMEM 类型/速度

51 SPD READING FAILED 读SPD失败

52 INV MEM SIZE/MODULESINV MEM尺寸/模组

53 NO USABLE MEM DETECT 不能应用MEM检测

54 MEM INIT ERROR MEM初始化错误

55 MEMORY NOT INSTALLED 内存不能安装

56 INV CPU TYPE/SPEED INVCPU类型/速度

57 CPU MISMATCH

58 CPU SELF TEST FAILEDCPU自检失败

59 CPU MICRO NOT FOUND 没找到CPU微代码

5A INTERNAL CPU ERROR 内部CPU错误

5B RESET PPI NOT AVAILPPI不能复位

5C AMI RESERVED AMI保留

5D AMI RESERVED AMI保留

5E AMI RESERVED AMI保留

5F AMI RESERVED AMI保留

60 DXE CORE STARTED DXE内核启动

61 NVRAM INITIALIZATIONNVRAM设定初值

62 INSTALL SB RUNTIME 安装SB运行期

63 CPU DXE INIT CPU DXE初始化

64 CPU DXE INIT CPU DXE初始化

65 CPU DXE INIT CPU DXE初始化

66 CPU DXE INIT CPU DXE初始化

67 CPU DXE INIT CPU DXE初始化

68 PCI HB INIT PCI HB初始化

69 NB DXE INIT NB DXE初始化

6A NB DXE SMM INIT NB DXESMM初始化

6B NB DXE INIT NB DXE初始化

6C NB DXE INIT NB DXE初始化

6D NB DXE INIT NB DXE初始化

6E NB DXE INIT NB DXE初始化

6F NB DXE INIT NB DXE初始化

70 SB DXE INIT SB DXE初始化

71 SB DXE SMM INIT SB DXESMM初始化

72 SB DEVICES INIT SB DXE设备初始化

73 SB DXE INIT SB DXE初始化

74 SB DXE INIT SB DXE初始化

75 SB DXE INIT SB DXE初始化

76 SB DXE INIT SB DXE初始化

77 SB DXE INIT SB DXE初始化

78 ACPI MODULE INIT ACPI模组初始化

79 CSM INIT CSM初始化

7A RESERVED AMI DXE AMIDXE保留

7B RESERVED AMI DXE AMIDXE保留

7C RESERVED AMI DXE AMIDXE保留

7D RESERVED AMI DXE AMIDXE保留

7E RESERVED AMI DXE AMIDXE保留

7F RESERVED AMI DXE AMIDXE保留

80 OEM DXE INIT OEM DXE初始化

81 OEM DXE INIT OEM DXE初始化

82 OEM DXE INIT OEM DXE初始化

83 OEM DXE INIT OEM DXE初始化

84 OEM DXE INIT OEM DXE初始化

85 OEM DXE INIT OEM DXE初始化

86 OEM DXE INIT OEM DXE初始化

87 OEM DXE INIT OEM DXE初始化

88 OEM DXE INIT OEM DXE初始化

89 OEM DXE INIT OEM DXE初始化

8A OEM DXE INIT OEM DXE初始化

8B OEM DXE INIT OEM DXE初始化

8C OEM DXE INIT OEM DXE初始化

8D OEM DXE INIT OEM DXE初始化

8E OEM DXE INIT OEM DXE初始化

8F OEM DXE INIT OEM DXE初始化

90 BDS STARTED BDS启动

91 DRIVER CONNECTING 硬盘连接

92 PCI BUS INIT PCI总线初始化

93 PCI BUS HOT PLUG PCI总线热插拔

94 PCI BUS ENUMERATIONPCI总线列举

95 PCI BUS REQUEST PCI总线请求

96 PCI BUS ASSIGN PCI总线分配

97 CONSOLE OUTPUT CON 控制台输出连接

98 CONSOLE INPUT CON 控制台输入连接

99 SUPER IO INIT 超级IO初始化

9A USB INIT USB初始化

9B USB RESET USB复位

9C USB DETECT USB检测

9D USB ENABLE USB允许

9E AMI RESERVED AMI保留

9F AMI RESERVED AMI保留

A0 ASL RESERVED ASL保留

A1 IDE INIT IDE初始化

A2 IDE RESET IDE复位

A3 IDE DETECT IDE检测

A4 IDE ENABLE IDE允许

A5 SCSI INIT SCSIE初始化

A6 SCSI RESET SCSIE复位

A7 SCSI DETECT SCSIE检测

A8 SCSI ENABLE SCSIE允许

A9 SETUP VERIFY PASSSETUP校验通过

AA ASL RESERVED ASL保留

AB START OF SETUP SETUP开始

AC SETUP INPUT WAIT SETUP输入等待

AD READY TO BOOT EVENT 准备启动环境

AE LEGACY BOOT EVENT 传统启动环境

AF EXIT BOOT SERVICES 退出启动服务

B0 VIRTUAL ADDR MAP BEG 虚拟地址图开始

B1 VIRTUAL ADDR MAP END 虚拟地址图结束

B2 LGCY OPTION ROM INIT 传统可选ROM初始化

B3 SYSTEM RESET 系统复位

B4 USB HOT PLUG USB热插拔

B5 PCI BUS HOT PLUG PCI总线热插拔

B6 CLEAN-UP OF NVRAM 清理NVRAM

B7 CONFIGURATION RESET 配置复位

B8 AMI RESERVED AMI保留

B9 AMI RESERVED AMI保留

BA AMI RESERVED AMI保留

BB AMI RESERVED AMI保留

BC AMI RESERVED AMI保留

BD AMI RESERVED AMI保留

BE AMI RESERVED AMI保留

BF AMI RESERVED AMI保留

C0 OEM BDS INIT OEM BDS初始化

C1 OEM BDS INIT OEM BDS初始化

C2 OEM BDS INIT OEM BDS初始化

C3 OEM BDS INIT OEM BDS初始化

C4 OEM BDS INIT OEM BDS初始化

C5 OEM BDS INIT OEM BDS初始化

C6 OEM BDS INIT OEM BDS初始化

C7 OEM BDS INIT OEM BDS初始化

C8 OEM BDS INIT OEM BDS初始化

C9 OEM BDS INIT OEM BDS初始化

CA OEM BDS INIT OEM BDS初始化

CB OEM BDS INIT OEM BDS初始化

CC OEM BDS INIT OEM BDS初始化

CD OEM BDS INIT OEM BDS初始化

CE OEM BDS INIT OEM BDS初始化

CF OEM BDS INIT OEM BDS初始化

D0 CPU INIT ERROR CPU初始化错误

D1 NB INIT ERROR NB初始化错误

D2 SB INIT ERROR SB初始化错误

D3 PROTOCOL NOT AVAIL. 协议不能获得

D4 PCI ALLOC ERROR PCI分配错误

D5 NO SPACE FOR OPROM 没有空间供OPROM

D6 NO CONOUT DEVICE 没有控制台输出设备

D7 NO CONIN DEVICE 没有控制台输入设备

D8 INVALID PASSWORD 无效口令

D9 ERROR LOADING BOOT 加载Boot错误

DA BOOT OPTION FAILEDBoot选项失败

DB FLASH UPDATE FAILEDFLASH更新失败

DC RESET PROTOCOL FAIL 复位协议失败

E0 S3 RESUME STARTED S3唤醒启动

E1 S3 BOOT SCRIPT EXEC 执行S3启动脚本

E2 VIDEO REPOST 视频重新POST

E3 OS S3 WAKE VECTOR OSS3待机导向

E4 AMI RESERVED AMI保留

E5 AMI RESERVED AMI保留

E6 AMI RESERVED AMI保留

E7 AMI RESERVED AMI保留

E8 S3 RESUME PEI FAIL S3唤醒PEI失败

E9 S3 PPI NOT FOUND 没有找到S3 PPI

EA S3 BOOT SCRIPT ERRORS3 启动脚本错误

EB S3 OS WAKE ERROR S3 OS待机错误

EC AMI RESERVED AMI保留

ED AMI RESERVED AMI保留

EE AMI RESERVED AMI保留

EF AMI RESERVED AMI保留

F0 RECOVERY - FIRMWARE 复原-固件

F1 RECOVERY - USER 复原-用户

F2 RECOVERY STARTED 复原开始

F3 RECOVERY FW STARTED 复原固件开始

F4 RECOVERY FW LOADED 复原固件加载

F5 AMI RESERVED AMI保留

F6 AMI RESERVED AMI保留

F7 AMI RESERVED AMI保留

F8 RECOVERY PPI NOT FND 复原 PPI 没找到

F9 RECOVERY CAP NOT FND 复原 CAP 没找到

FA INVALID RECOVERY CAP 复原 CAP 无效

FB AMI RESERVED AMI保留

FC AMI RESERVED AMI保留

FD AMI RESERVED AMI保留

FE AMI RESERVED AMI保留

FF AMI RESERVED AMI保留